## Slide 1: Photoresistor
Raspberry Pi Chapter 10

## Slide 2: Photoresistor
Also known as LDR (Light Dependent Resistor)
Resistance changes based on intensity of light
  Light intensity measured in lux
The higher the light intensity, the lower the resistance

## Slide 3: Specifications
Cost: $7.95 for a pack of 5 (Sayal)

## Slide 4: How it Works
Made of a semiconducting material that has a rigid hold on electrons
When light hits the semiconducting material, the electrons break free, conducting electricity
This decreases resistance

## Slide 5: Intrinsic vs. Extrinsic Photoresistor
Intrinsic – pure semiconductor material
  Electrons jump from outer valence shell to inner shell
Extrinsic – semiconductor materials with impurities
  New orbital is created, electrons move from outer shell to orbital
  Used for longer wavelengths, e.g. infrared

## Slide 6: Applications
Streetlight
Security System – Bank, Jewellery Store
Car Headlights
Alarm Clocks

## Slide 7: Wiring a Photoresistor
Voltage Divider Circuit
  10 kΩ resistor – used as a reference point
Current is constant at all points of the circuit
  Ohm’s law: Et = Irt
  Rearranging to solve for current: I = Et /Rt
  Voltage drop across the photoresistor: En = Et /Rt x Rn
    En = Et x Rn/Rt