## Slide 1: Relays
Raspberry Pi Chapter 14

## Slide 2: Relay – Use and Purpose
An electromagnetic switch
  Controls a circuit using current flow
Use a low power circuit to control a high power circuit
  Low power – microcontroller, digital logic
  High power – Actuator circuit
Can be used as amplifier

## Slide 3: How a Relay Works
Electrical current magnetizes coil
  Coil is an inductor – converts electrical to magnetic energy
  Unit – inductance, measured in Henrys (H)
Coil attracts armature, which lowers contact to connect circuit

## Slide 4: Relay Pinout
Pin | Purpose
1 | Closed contact
2 | Open contact
3 | Connects to inductor coil
4 | Connects to inductor coil
5 | Connects to actuator & pin 6
6 | Connects to actuator & pin 5
Specs: Trigger voltage – 5V
Maximum DC voltage and current: 24V, 3A
Maximum AC voltage and current: 120V, 3A

## Slide 5: Circuit

## Slide 6: Applications of Relays
Automotive Relays – turning on the starter motor, headlights, etc. at the same time
Power bar – If AC current is detected, connect to transformer circuit to provide DC power
Buildings – Heating, cooling, lights, etc.