## Slide 1: PWM
Raspberry Pi Chapter 4

## Slide 2: Purpose
Digital signals – two values, either logic high or low
Analog signals – continuous signal, can have floating point values
PWM – Pulse width modulation
  Uses digital signals to represent an analog signal
  Usage: control brightness of LED, speed of DC motor

## Slide 3: Terminology
Period – length of time for one set of a logic high and logic low pulse
Frequency – number of sets of a logic high and low pulse for a given amount of time (1/period)
  Affects resolution
Pulse width – length of time for a logic high signal
Duty cycle – percentage of period for which a signal is logic high

## Slide 5: Hardware vs. Software PWM
Hardware
  Uses microprocessor to generate pulses
  Accurate timing, does not use CPU resources
Software
  Emulates PWM
  “On”, delay, “Off” in a loop
  Uses CPU resources, inaccurate timing
Raspberry Pi GPIO 18 – 10 bit accuracy software PWM